## Slide 1
Fix using Arduino
Anet A8 Bricked Bootloader

## Slide 2
Wiring

## Slide 3
1. Upload ArduinoISP sketch to Arduino Uno board (File -> Esempi)
2. Select from Arduino Tools menù:
  a. Board:Arduino Uno
  b. Port: COM X where your Arduino is connected
  c. Programmer: AVRISP mkll
3. Upload Sketch
Arduino now is ready to act as ISP Programmer
PREPARE ARDUINO UNO AS ISP PROGRAMMER

## Slide 4
1. Select from Arduino Tools menù:
  a. Board:Anet V1.0 (Optiboot)
  b. Port: COM X where your Arduino is connected
  c. Programmer: Arduino as ISP
2. Tools -> Write Bootloader
FLASH BOOTLOADER

## Slide 5
1. Select from Arduino Tools menù:
  a. Board:Anet V1.0 (Optiboot)
  b. Port: COM X where your Arduino is connected
  c. Programmer: AVRISP mkll
2. Open Marlin firmware as usual
3. Upload sketch
UPLOAD FIRMWARE